## Slide 1
ANALOG LINE FOLLOWING ROBOT
www.reallygreatsite.com
Presented by Outlaws

## Slide 2
  Fully analog line-following robot using PID control.
  IR sensor array detects line position.
  Analog circuits generate error and implement PID.
  Comparator with triangular wave produce PWM for motor control.
  Transistors drive motors for smooth, real-time line tracking.
Project Overview

## Slide 3
Components and Selection
Provides accurate line position detection. Analog output simplifies processing.
3.7 V Li-ion Batteries
IR Sensors
Used as the main power source. Two batteries connected in series supply sufficient voltage for both regulators to produce ±5 V.
Contains 4 op-amps in total. Ideal for implementing P, I, D circuits and signal conditioning.
LM324N Op-Amp IC
Used for filtering, integration, and differentiation circuits.
Capacitors
Used to create a regulated ±5 V dual power supply for stable analog operation.
Voltage Regulators
Used for setting PID gains (Kp, Ki, Kd) and voltage division.
DC Motors
MOSFETs
Resistors & Variable resistors
Provide motion to the robot and respond effectively to PWM control signals.
Used as efficient electronic switches for driving DC motors with PWM signals. Offer fast switching speed and low power loss compared to BJTs.
The buck converter steps down the battery voltage to a stable 6 V supply, ensuring efficient and reliable power delivery to the DC motors without affecting the analog control circuits.
Buck Converter

## Slide 4
System Block Diagram
Amplifier

## Slide 5
Functionality
Buffer Circuit
Function: Detects the position of the black line on a white surface.Provides analog voltage proportional to reflected light intensity.
Component: 8 IR emitter–receiver pairs.
IR Sensor Array
Function: Isolates the sensor array from the next stage and prevents signal interference.
Component: Op-amps from LM324 in voltage follower mode.
Input IR sensors and buffers

## Slide 6
Functionality
Scaling adders and Subtractor
Weighted Sum Calculation
Function: Computes position information by giving different weights to each sensor.
Component: Scaling adder circuit using op-amps and resistors.
Calculate Difference
Function: Produces the error signal by comparing left and right sums.
Component: Differential amplifier

## Slide 7
PID Control
  Proportional (P): Directly amplifies error signal.
    Provides immediate correction proportional to error.
  Integral (I): Integrates error over time using an op-amp integrator.
    Eliminates steady-state error.
  Derivative (D): Differentiates error signal using an op-amp differentiator.
    Predicts and reduces overshoot.
PID controller
Proportional
Derivative
Integral
Functionality

## Slide 8
Transistor Switch
Function: Drives DC motors based on PWM signal.
Component: Power transistors
Motors
Function: Execute movement and correction.
Component: Two DC gear motors.
Motor controlling circuit
Functionality

## Slide 9
Triangular wave generator
Comparator
Function: Produces a periodic triangle waveform.
Component: Op-amp-based integrator + comparator.
Triangle Wave Generator
Function: Compares PID output with triangle wave to generate PWM.
Component: Op-amp in comparator mode.
Functionality

## Slide 10
Regulators and power management circuits

## Slide 11
PCB Design

## Slide 12
Enclosure Design

## Slide 14
THANK YOU!
www.reallygreatsite.com